## Slide 1
Maxime Lefrançois
MINES Saint-Etienne, CNRS,
Laboratoire Hubert Curien UMR 5516
The SEAS Ontology(ies)
https://w3id.org/seas/
Maxime Lefrançois, Jarmo Kalaoja, Takoua Ghariani, Antoine Zimmermann, The SEAS Knowledge Model, ITEA2 12004 Smart Energy Aware Systems Deliverable 2.2, Jan 2017
For now, please use:

## Slide 2
WP 1 - use cases, business models, requirements, architecture
WP 2 - knowledge model, knowledge based services
WP 3 - Smart Building
WP 4 - Microgrids, and Electric Vehicles
WP 5 - Simulations
WP 6 - Prototypes and Pilots
WP 7 - Standardization
Design and develop a global ecosystem of distributed services that all target energy efficiency.
Feb 2014 - Dec 2016
3 years, 6 countries, 34 partners, 16M€, 160 person-year
ITEA Award of Excellence 2017
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 3
Demands, offers, transactions
Contracts for demand-response or aggregators
The infrastructures characteristics and limitations
Energy generation/load/storage/transfer
Smart Building zones and environmental factors
Smart Building and its interaction with the environment
Controllable and non-controllable appliances / loads
Controllable and non-controllable energy generators
electric vehicles and charging equipment
Characteristics specific to batteries
Time series: history, observations, forecast
Data privacy and access control – contracts
Describing very light messages sent to/from sensor/actuators
Describing SEAS service and their interfaces to ease their registration and discovery
Domains to be modelled
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 4: Several ontologies exist
Or were under development in 2015 (SAREF)
They are often not open source and extensible
They use custom and unpredictable RDF structure
They do not cover all of the domains we need
We needed a simple core that:
  covers most of the partner needs,
  can be implemented easily in OOP,
  can be extended to other domains.
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 5: Ease their extension to other domains ? simple core + extensible + open-source
Smart Grid
Core of SEAS
Ontology patterns
Simple
Transport
Smart Home
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 6: Ease their extension to other domains ? simple core + extensible + open-source
Smart Grid
Core of SEAS
Ontology patterns
Simple
Transport
Smart Home
Building
HVAC
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 7: Main source of inspiration: the SSN ontology
W3C, next version should be released late June 2017
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 8: Main source of inspiration: the SSN ontology
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 9
the Property ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 10
<car/1> a ex:MovingThing ;
seas:hasProperty <car/1/speed> .
ex:speed a owl:ObjectProperty , owl:FunctionalProperty ;
rdfs:subPropertyOf seas:hasProperty ;
rdfs:domain ex:MovingThing ;
rdfs:range ex:SpeedProperty .
the Property ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 11: Main source of inspiration: the SSN ontology
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 12: the Process Execution ontology pattern
Disclaimer: naming may be updated depending on the discussions with W3C
i.e., former terms will be deprecated, not removed
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 13: the Process Execution ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 14: the Process Execution ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 15: the Process Execution ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 16: the Process Execution ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 17: Main source of inspiration: the SSN ontology
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 18: the Evaluation ontology pattern
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 19: the Evaluation ontology pattern
Extensible taxonomy
Instead of duplicating « hasProperty » sub-properties,
-> us a single « hasProperty » sub-property, and one or more sub-classes of Evaluation
-> <fridge/1/consumption> + AverageEvaluation;
<fridge/1/consumption> + NominalOperatingEvaluation;
<fridge/1/consumption> + ReductionFlexibilityEvaluation;
<fridge/1/consumption> + …
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 20: the Evaluation ontology pattern
Use QUDT, OM, custom ontology,…
Use literals, custom literals…
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 21: Main source of inspiration: the SSN ontology
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 22: the System ontology pattern
E
E 800 W
E
E €
Qualify systems
  The environment in a specific place
  A building, a room
  An appliance
  A set of appliances
  A business partner
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 23: the System ontology pattern
E
E 230 V
E €/MWh
offer/demand
Qualify systems
  The environment in a specific place
  A building, a room
  An appliance
  A set of appliances
  A business partner
Qualify their connection points
  Wall, window, ceiling
  Plug, Socket
  Offer, demand
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 24: the System ontology pattern
Qualify systems
  The environment in a specific place
  A building, a room
  An appliance
  A set of appliances
  A business partner
Qualify their connection points
  Wall, window, ceiling
  Plug, Socket
  Offer, demand
Qualify the connections between these systems (flows)
  Electric energy flows
  Water volume/ thermic energy / light flows
  ...
E
E 400 A
E - km/h
E - thermic energy / power
E
€
MWh
penalties
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 25: Current modules
(IT) ArchitectureOntology,
BatteryOntology,
BooleanPropertyOntology,
BuildingOntology,
ComfortOntology,
CommunicationOntology,
ComplexOntology,
DeviceOntology,
ElectricLightSourceOntology,
ElectricPowerSystemOntology,
ElectricVehicleOntology,
EnergyFormOntology,
EvaluationOntology,
FailableSystemOntology,
FeatureOfInterestOntology
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 26: Example of extension: HVAC, Mads Holten Rasmussen, Alectia
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 27
Example of extension: HVAC, Mads Holten Rasmussen, Alectia

## Slide 28
Example of extension: HVAC, Mads Holten Rasmussen, Alectia

## Slide 29
Example of extension: HVAC, Mads Holten Rasmussen, Alectia

## Slide 30
Example of extension: HVAC, Mads Holten Rasmussen, Alectia

## Slide 31: Publish in conformance with the best practices ?
Follow the recommended best practices for metadata and access
Modular,
Versioned,
One single namespace for all SEAS concepts
https://w3id.org/seas/
+ Register on prefix.cc, the LOV, …
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 32: Ease the contributions from experts ?
Open source on GitHub https://github.com/thesmartenergy/seas
Use automatic quality checking tools
  Naming conventions,
  Metadata existence and consistence,
Use automatic pattern instantiation techniques
  Ongoing, release planned April 2017
Use continuous integration techniques on GitHub
  Ongoing, release planned April 2017
Maxime Lefrançois – the SEAS ontology: instantiating ontology-patterns

## Slide 33: Ease the contributions from experts ?
Workshops with domain experts to promote Linked Data, and extend SEAS to a specific domain

## Slide 34
Maxime Lefrançois
MINES Saint-Etienne, CNRS,
Laboratoire Hubert Curien UMR 5516
The SEAS Ontology(ies)
https://w3id.org/seas/
Maxime Lefrançois, Jarmo Kalaoja, Takoua Ghariani, Antoine Zimmermann, The SEAS Knowledge Model, ITEA2 12004 Smart Energy Aware Systems Deliverable 2.2, Jan 2017
For now, please use: